## Slide 1: Horticulture II - Landscape
Unit c landscape installation and maintenance

## Slide 2: Objective 6.03
Apply procedures to maintain turfgrass

## Slide 3: Procedures for Irrigating Turfgrass

## Slide 4: Irrigating Turfgrass
Step 1 – Determine need for water by the turf
  Use visual appraisal and turf knowledge to determine the need for water
    Are there indications that it is time to irrigate?
      Has there been an extended period of time since the turf has received water?
      Does the grass have a dark bluish-gray color?
      Do footprints remain some time after walking occurs across the grass?
      Does the grass exhibit wilted, folded, or curled leaves?
    Use a soil probe to determine how deep the soil is moist
      Moisture meters can also be used for this purpose

## Slide 5: Irrigating Turfgrass
Step 2 – Determine the amount of water the irrigation system is delivering
  Collect water using several rain gauges or gallon cans spaced evenly throughout the irrigation area
  Water the area for a determined interval (30 minutes is the minimum the area should be watered) and record the time
  Read the inches in each rain gauge or use a ruler to measure the inches in each gallon can
  Average the water in each can by totaling the inches of water collected and dividing by the total number of cans or gauges
  Record the average water collected for all gauges or cans

## Slide 6: Irrigating Turfgrass
Step 3 – Determine the amount of water needed by the turf
  Use the (TIMS) Turf Irrigation Management System
    (http://www2.turffiles.ncsu.edu/tims/Default.aspx?ReturnUrl=%2fWaterCalc.aspx)
    Create a user name and password for the system and store it for future reference
    Complete personal data and click next with the mouse
    Select soil type and click next with the mouse
    Select the type of turf to be irrigated and click next with the mouse
    Calculate the irrigation water rate by inserting the time interval and average inches of water collected per can or gauge
    Read irrigation recommendation from the screen

## Slide 7: Irrigating Turfgrass
Step 4 – Turn water control on to apply water during early morning
  Monitor the area for runoff and water standing
    If runoff is observed, turn the system off and wait for at least 30 minutes before continuing
    If water is standing on the grass, turn the system off and wait for at least 30 minutes before continuing or until existing water has been absorbed into the soil (whichever is longer)
    Continue irrigation to rewet the soil until the water reaches the appropriate depth
      Sloped areas, compacted soils, and sandy soils need to be irrigated for shorter times, but at more frequent intervals
  Monitor the irrigation system for uniform distribution
    Are all sprinkler heads working properly?
    Are there areas that sprinkler heads are not reaching?

## Slide 8: Irrigating Turfgrass
Step 4 – Continued
  Stop water after the appropriate water has been applied
    Cut water off when the time interval recommended by TIMS has been achieved or visual appraisal indicates the turf has been watered enough
    Water until the soil is moist to a depth just below the root system to encourage further rooting
      Use a soil probe to make a visual estimation of the depth of soil moisture
      Use a moisture meter to determine the depth of soil moisture
        Watering deeper does not benefit the plant and may leach contaminants into the groundwater

## Slide 9: Procedures for Mowing Turfgrass

## Slide 10: Mowing Turfgrass
Step 1 – Determine if the grass needs mowing
  Visually inspect the grass to determine if mowing will improve the appearance or function for which the grass is intended OR
  Refer to http://www.turffiles.ncsu.edu/ and click on Carolina Lawns
  Click on the Printable PDF link to open the publication
  Consult Table 2 (Carolina Lawns) to determine the optimum height for the grass to be mowed
  Add 50% to the maintenance height. (Example: if tall fescue is being mowed at 3” as the maintenance height, 3” + 1.5” = 4.5” is the optimum height before mowing)
  Measure the grass to determine its height

## Slide 11: Mowing Turfgrass
Step 2 – Select the mower based on function of the grass and maintenance height of grass to be mowed
  Select reel type mower for extremely close cuts and highly managed turf on golf courses and athletic fields
  Select rotary type mowers for general purpose lawn care

## Slide 12: Mowing Turfgrass
Step 3 – Inspect the blade(s) prior to mowing and if needed, sharpen
  Visually inspect the blades for nicks, signs of wear, and dullness
  Carefully feel the blade to determine if a cutting edge exists
  Refer to Owner’s Manual for instructions to remove blade(s)
  Remove blades per instructions
  Sharpen blades according to proper procedure specified in Objective 6.04
  If blades are heavily worn or damaged, discard and replace with new blades

## Slide 13: Mowing Turfgrass
Step 4 – Determine whether to bag or mulch clippings
  If clippings are excessive, the will smother or shade the growing turf. Always remove clippings in this situation by bagging or raking
  If clippings are not excessive, always cut with a mulching blade and allow to remain on the turf surface to provide additional nutrients
  Visually inspect the nature and amount of clippings from a sample cut to determine if bagging is necessary and act accordingly

## Slide 14: Mowing Turfgrass
Step 5 – Mow the grass
  Follow the instructions in the unpacked content for starting the small engine found in Objective 5.02
  Follow all safety procedures for engaging the blade(s) and operating the mower safely per the owner’s manual for the selected mower

## Slide 15: Procedures for Applying Maintenance Fertilizer to Turfgrass

## Slide 16: Fertilizing Turfgrass
Step 1 – Use soil test to determine the amounts of lime and fertilizer needed (preferred option)
  Follow procedure found in Objective 5.03 for Soil Sampling
  Determine fertilizer needs based on the Soil Test Report

## Slide 17: Fertilizing Turfgrass
Step 2 – Use recommendations from Turffiles to determine the level and timing of fertilizer application
  Consult Carolina Lawns section on “Fertilizing”, “Fertilizing after Planting”, and Tables 6a, 6b, or 6c to determine the fertilizer needs for lawn maintenance
  Use the Turffiles website to consult maintenance calendars for athletic fields, etc. at : http://www.turffiles.ncsu.edu/Maintenance_Calendars.aspx#
Step 3 – Apply the fertilizer
  Use technique learned in Objective 5.03 to spread the fertilizer

## Slide 18: Procedures used to Alleviate Unique Turfgrass Cultural Problems

## Slide 19: Cultural Control
Step 1 – Determine what cultural problems need to be treated
  Is soil compaction an issue?
  Is excessive thatch build up an issue?
Step 2 – Select appropriate equipment to treat cultural problems
  What types of equipment can be used to treat soil compaction?
  What types of equipment can be used to treat thatch build-up?
  Is it the best time to treat cultural problems?
  What pattern should be followed when treating the cultural problem?
Step 3 – Use appropriate equipment in the prescribed manner to treat cultural problems
  Follow operator’s manual for the selected equipment to operate equipment safely
  Follow manufacturer’s recommendation on the procedures to most effectively use the equipment