## Slide 1: Horticulture II - Landscape
Unit c landscape installation and maintenance

## Slide 2: Objective 6.04
Apply procedures to maintain landscape equipment and tools

## Slide 3: Procedures to Select PPE Appropriate for Specific Tasks
Determine the potential hazard
Identify PPE needed to protect against potential hazard
Select the identified PPE
Check to be certain PPE is clean and in good repair

## Slide 4: Procedures to Select PPE Appropriate for Specific Tasks
Put on the PPE
  If safety glasses are the identified PPE, put on safety glasses to cover eyes before beginning task or if watching someone perform the task
  If goggles are the identified PPE, put on goggles or use face shield to protect more than eyes or if workers is wearing prescription glasses (not safety glasses)
  If leather gloves are the identified PPE, slip each hand into a glove before beginning a task that could burn the hands
  If chemical gloves are identified PPE, slip each hand into a glove before beginning a task using chemicals

## Slide 5: Procedures to Conduct Pre-operation Inspection
Check to make sure cooling fins are not obstructed by debris
Clean if obstructed
Check oil and fluid levels
Fill to recommended levels on dipsticks and tanks
Remove gas cap
Fill fuel tank to approximately 1”-½” below top of neck being careful not to overfill
Replace the gas cap before starting the engine
Check belts and chains for proper tension
Adjust as needed (Return to Owner’s Manual for specifications)

## Slide 6: Procedures to Conduct Routine Maintenance
Refer to Owner’s Manual for specifications and procedures because makes and models differ on both specifications and procedures for specific routine maintenance procedures
Use chart to maintain records of maintenance
  Date
  Maintenance performed
  notes
Determine from maintenance chart when scheduled maintenance should be done according to Owner’s Manual recommendations

## Slide 7: Procedures to Conduct Routine Maintenance
Change oil and filter. Follow engine manufacturer’s recommendations for change intervals and oil type viscosity and volume
  NOTE – small engines should have their oil changed every 25 houyrs and more frequently in dusty conditions
Clean or replace air filter every 25 hours or more frequently in dusty conditions
Replace dull or badly worn blades (See Owner’s Manual for procedures)
Adjust belt and chain tension as recommended by manufacturer in Owner’s Manual
Record in the chart the maintenance performed for future use

## Slide 8: Procedures to Maintain Hand Tools-Leather
Clean by rubbing with saddle soap
  Brush off all dirt
  Moisten cloth with water
  Rub moist cloth on saddle soap until suds make lather
  Rub suds into leather until leather is clean and soft
  Remove suds with a damp cloth
  Let leather dry
  Rub leather with a dry cloth
Restore and protect by using neat’s-foot oil or mink oil
  Apply neat’s-foot oil or mink oil with a soft cloth to restore and protect leather
  Remove excess oil with a soft cloth

## Slide 9: Procedures to Maintain Hand Tools-Wood
Sand with fine sandpaper to remove rough areas
Clean the surface until it is free of dust, dirt, and oil
Use a cloth to rub boiled linseed oil or paste finishing wax on handles and other wood parts to help repel water
  Boiled linseed oil
    Rub oil on wood with a clean cloth
    Allow 5-10 minutes for oil to penetrate wood
    Remove excess by wiping off with a clean, dry cloth
  Paste finishing wax
    Apply a thin coat of wax with a clean cloth
    Allow wax to dry 10-15 minutes
    Polish with a clean, dry cloth, a buffer, or a polisher

## Slide 10: Procedures to Maintain Hand Tools-Metal
Remove grease and oil with kerosene or other commercial solvent
Remove dirt with a scraper, wire brush, or wire wheel
Remove rust with kerosene or other solvents. May need a wire brush, wire wheel, steel wool, or emery cloth to remove pitting
Use a cloth to coat with light to medium weight oil
Protect from rust with rust-resisting primer and/or paint or paste wax
Lubricate joints with lightweight oil
Remove all metal burrs and rough spots with metal file or grinder

## Slide 11: Procedures to Maintain Hand Tools-Metal
Sharpen cutting edges with a metal-cutting file or grinder
  Digging tools such as shovel, spades, and hoes
    If the metal is curled back, place the tool on an anvil and tap bent metal back into place
    Use metal-cutting file or a grinder to sharpen on same side and at same angle as original bevel of cutting edge

## Slide 12: Procedures to Maintain Hand Tools-Metal
Sharpen cutting edges with a metal-cutting file or grinder
  Lawn mower blades
    Maintain original angle if known. If not known, grind or file to a 45 degree angle on the cutting side
    Keep or make other side flat (no angle)
    Remove same amount from both ends of the blade to maintain balance
    Place hole of blade on blade balancer to determine if balanced
    If not balanced, grind or file off enough from the low end of the blade to balance the blade